## Slide 1: FDSN Working Group III Agenda
12:00 Welcome and Introductions
Sign in sheet
Approval of 2013 WG III Minutes
Review of Charter for WG III
  Any suggested modifications to charter
12:15 Review of Existing FDSN Services and possible changes? Related to service interfaces not XML
Event service modifications
Station service modifications
Dataselect
Recommendations for New FDSN Services
12:30 FEDERATING THE FDSN DATA CENTERS
Status and Expansion of Federated Data Centers
    Status in Europe and Future Plans (powerpoint 2) Strollo/Pequegnat
  IRIS plans Ahern
  Other known efforts (Asia, North America, Latin America) Ahern
Review of the IRIS Federator with a short demonstration Trabant
Creating an FDSN Federator Ahern
  Business Rules Establishing Primary and Other Centers
  Considerations that should be included

## Slide 2: FDSN Working Group III Agenda (cont)
13:15 FDSN QUALITY ASSURANCE
Overview of Quality Assurance Efforts in the FDSN
Plan from 2013 was to see how MUSTANG develops – current status Ahern
IRIS MUSTANG – implementation as services Ahern
EIDA QA Status (powerpoint 3) Trani
FDSN Quality Assurance
FDSN Coordination – possible needs
Service definitions for metrics
  XML definitions
Sharing Algorithms for metrics
14:15 PRODUCTS
Review of products across the FDSN
  EIDA (powerpoint 4) Strollo
  IRIS (mention of DOIs) Trabant
  Other groups
14:45 DOIs
Status of DOIs for Seismic Networks Ahern
Other activities in the FDSN regarding DOIs
DOIs – what is next?
How do we get networks to mint DOIs and register them with the FDSN
15:00 ADJOURN

## Slide 3: FDSN WG III
Approval of 2013 WG III Minutes
Review of Charter for WG III
  Will coordinate the production of standard products and the methods for producing these products,
  Will coordinate the identification, development and/or distribution of standard software applications used to acquire, manage, distribute, and use data from FDSN data centers,
  Will coordinate the development and adoption of standards for services, including web services and other data center services, that are supported and deployed at FDSN centers.

## Slide 4: Review of Existing FDSN Services and needed changes? (Related to service interfaces not XML)
Event service modification
Station service modifications
Dataselect
  Match timeseries option
Recommendations for New FDSN Services
  Timeseries as a standard service of the FDSN
  SAC P&Z and RESP service
  Rotation Service
  Metadata changes service

## Slide 5: Status of FDSN Services
EIDA status
IRIS/US Status
IRIS Plans related to CoopEUS

## Slide 6: IRIS – US and non-European Services
Plans to Deploy Services – work started
  Canada, SCEDC, New Zealand
Plan to Deploy Services – no work started
  Mexico, interest in LACSC area
IRIS CoopEUS Activities
  Plan to hold workshop to promote Federated Centers in Western Pacific and SE, NE, Central Asia
  CAS, CENC, KMA (Korea), Japan, Taiwan, New Zealand, several partners in SE Asia

## Slide 7: IRIS Federator: Facilitating cross-center data access
FDSN dataselect and station services running at 13 data centers
(more coming):

## Slide 8: IRIS Federator Overview
Two main components:
Composite catalog of time series channels
  Updated nightly
Service for querying the catalog:
  http://service.iris.edu/irisws/fedcatalog/1/
The fedcatalog service is designed support client-side federation. The user’s data collection software contacts each center directly to retrieve data. Time series and related metadata do not flow through a central node.
Federation capability is being integrated into DMC tools and community-developed toolkits.

## Slide 9: IRIS Federator Removing duplicates
By default, but can be overridden, the IRIS Federator removes any duplicated channels in a result set as a service to the user. This is implemented using a flexible set of rules and is used to direct data requests to the primary data centers whenever possible.
These rules have greater granularity than NetDC
Rule tests can be network, station, location, channel and/or time window. In the IRIS Federator currently it is by Network and Time only in its early stages
GEOFON: GE ORFEUS: NL RESIF: FR
NCEDC: BK,NC SED: CH INGV: MN,IV,GU
KOERI: KO BGR: GR IPGP: G
LMU: BW NIEP: RO USPSC: BL,BR,Y4(2013)
IRIS: many other permanent and temporary networks/experiments

## Slide 10: Demonstration of Federator – Internet Willing

## Slide 11: Current Status in Europe related to a Federator/Moderator
    Powerpoint 2 from Catherine Pequegnat

## Slide 12: Developing an FDSN Federator
Developing the Rules
What things should be considered
  Reliability
  Politics
  Proximity
  Scalability
What role do secondary centers play?

## Slide 13: Quality Assurance
2013 plan from Gothenburg was to see how MUSTANG would develop
Status of MUSTANG

## Slide 14: What is MUSTANG?
MUSTANG is an automated data quality assurance system that stores measurements of seismic data quality for the entire IRIS archive (in progress) and makes them available to the community through web services.
Currently, 45 metrics are calculated.
The system is modular; new metrics can be added readily.
MUSTANG will have the capability to automatically update metrics values when the data, metadata, or algorithms change.
MUSTANG Presentation on Wednesday at 13:45 in
Session S01g/S11

## Slide 15: The MUSTANG System
Web service call
Other communication
MUSTANG clients
Other Analysis software
Text-based data
graphics
Metrics updater
Metrics scheduler
Metrics job
Metrics job
Metrics job
Metrics database
MUSTANG
Contributed metrics
IRIS SEED Archive
Real time
miniseed
Metadata
database
miniSeed
archive
MUSTANG Databrowser
LASSO
Scripts etc

## Slide 16: MUSTANG 46 Metrics Available
* in development

## Slide 17: service.iris.edu/mustang/

## Slide 18: MUSTANG Web Services
http://service.iris.edu/mustang

## Slide 19: Automated Text Reports for internal analyst use
Created by script using MUSTANG metrics
Groups metrics into problem types
Quick way to focus on problem stations for further review

## Slide 20: Example: Response Error Found Using the pct_below_nlnm Metric
(the percent of PSD values that are below the New Low Noise Model)
HHE poles:
HHN poles:
Sign error
X

## Slide 21: Example: Data Completeness
Box plot illustration from Wikipedia
percent_availability metric (channel percent available per day)
MUSTANG Databrowser Network Boxplots

## Slide 22: Example: Channel Orientation Analysis
The orientation_check metric finds observed channel orientations for shallow M>= 7 events by
  Calculating the Hilbert transform of the Z component (H{Z}) for Rayleigh waves
  Cross-correlating H{Z} with trial radial components calculated at varying azimuths until the correlation coefficient is maximized
  The observed channel orientation is difference between the calculated event back azimuth and observed radial azimuth
Stachnik, J.C., Sheehan, A.F., Zietlow, D.W., Yang, Z, Collins, J. and Ferris, A, 2012, Determination of New Zealand Ocean Bottom Seismometer Orientation via Rayleigh-Wave Polarization, Seismological Research Letters, v. 83, no. 4, p 704-712.
X

## Slide 23: Network Operator Reports
Prototype of final product after analyst review verifying accuracy of station issues
Virtual network report
summarized by network
Links to analyst assessment of issue

## Slide 24: What is MUSTANG’s biggest challenge

## Slide 25: QA Efforts within EIDA
Powerpoint 4- Strollo

## Slide 26: Data Products
Efforts at the IRIS DMC

## Slide 27: Higher level data products
http://ds.iris.edu/ds/products/
USArray ground motion visualizations
Event plots
Aftershock sequences
EQ energy & duration
Source-time functions
Back projections
ShakeMovie 3D synthetics
And more…
Receiver functions
Earth Model Collaboration
Infrasound (USArray TA)
  Reference event database
  Detection catalog
Global CMT solutions
Ambient Noise CCs
Empirical Greens Tensors
Surface wave phase velocity measuring system

## Slide 28: EMC 3D Visualization
Relatively simple, Python-based Earth model desktop visualization tool.
Designed for IRIS EMC models, but works with general netCDF volumes.
Come see the poster.

## Slide 29: Data Product Usage
Average data product access rate: 4-6 per hour

## Slide 30: Data Product Usage
Peak activity is event-related, e.g. 2015-5-25 Nepal M 7.8

## Slide 31: FDSN Digital Object Identifiers
IRIS has revamped the FDSN Network pages significantly
  Off of Oracle and into PostgreSQL
  The FDSN is totally isolated from DMC operations through a dedicated virtual machine
Requesting a Network Code
  http://www.fdsn.org/networks/request/perm/
Now has a section related to NETWORK CITATIONS

## Slide 32: Totally FDSN Branding
http://www.fdsn.org/networks/request/perm/

## Slide 33: Previous information is now augmented with Network Citation

## Slide 34: FDSN Networks Page http://fdsn.org/networks/

## Slide 35: Example Landing Page

## Slide 36: Stations lists and maps generated dynamically using FDSN services if availble

## Slide 37: Another Example with Publications

## Slide 38: Important Next Steps for DOIs
Let people know some exist
IRIS DMC will include DOIs in qurterly summaries sent to
  Users receiving data from the IRIS DMC
Permanent networks
  366 network codes assigned
  22 DOIs
Temporary Networks
  767 network codes assigned
  11 DOIs